## Slide 1
AqOne Detailed Architecture
Offline SOS transport, safety intelligence and responder loop
SOURCE BUILT. FIELD VALIDATION PENDING
Input and Field Layer
Evidence sources and human actions
Edge and Transport Layer
Store first, forward when a path exists
Backend and Data Layer
Provider-neutral logical architecture
Processing and Decision Support Layer
Manual SOS remains independent of every model
Output and Human Response Layer
Human authority remains explicit
Fisher mobile app
Manual SOS, GPS, timestamp, trip check-ins, optional catch logs
Boat pod
Physical SOS button, GNSS, battery and radio events
Stationary sensor buoy
Fixed pressure, current observations and device health
Environmental data
Open-Meteo weather and marine observations
Responder actions
Acknowledge, ETA, resolution and searched sectors
Mobile SQLite outbox
Persists an SOS before any network attempt Delivery state: SAVED
Direct internet path
HTTPS when cellular or WiFi internet is available
Boat pod flash queue
Accepts before acknowledgement and retries after outages Delivery state: RELAYED
Optional relay buoy
TTL flooding and duplicate suppression only where field tests justify it
Tall shoreline gateway
Verifies LoAM signature, maps device identity and forwards over HTTPS
Return path
Warnings, acknowledgement and ETA when radio or internet is available
WIFI HTTP
DIRECT LoRa
OPTIONAL RELAY
FastAPI application services
Authentication and roles, validation and deduplication, SOS and sensor ingest, incident and advisory workflows
PostgreSQL
SOS and responder actions Trips and contact events Sensor, advisory, model and audit records
Current dashboard path: protected REST polling every 3 seconds
AUTHENTICATED HTTPS
Manual SOS
AI-independent emergency path
Environmental warning
Squall and marine danger
Trip anomaly
Overdue verification support
Drift and search
Physics-based decision support
Consented catch activity
Separate optional data purpose
Validate and deduplicate
Accept distress even before vessel registration
Persist incident
Backend becomes authority for DELIVERED
Responder workflow
Acknowledge, ETA, reply and resolution
DELIVERED / ACKNOWLEDGED
Quality and freshness gate
Reject stale, missing or insufficient observations
Two distinct models
Backend squall nowcast Browser danger-zone GBDT
Advisory candidate
Shows source, age, confidence and limitations
WARNING CANDIDATE
Contact and trip history
Only observations at or before decision time
Per-vessel profile
Compares duration and route against that vessel
Verification and escalation
Silence alone never proves distress
RESPONDER REVIEW
Confirmed incident datum
Last reliable fix, object class, wind, current and coastline
Monte Carlo leeway
Particle paths with land stranding and uncertainty
Search posterior update
Negative search evidence shifts remaining probability
SEARCH CONTOURS 50 / 75 / 95%
Explicitly consented logs
Safety access never depends on participation
Privacy aggregation
Coarse cells and minimum independent reporters
Recent activity surface
No guaranteed catch and no exact public locations
COARSE ACTIVITY
MODEL OUTPUTS ADVISE; AUTHORIZED PEOPLE DECIDE
Squall calibration is synthetic. Drift awaits live buoy current telemetry. Catch workflow remains a pilot foundation.
Fisher mobile app
Delivery states and responder ETA Warnings and forecast freshness Optional coarse activity
MDRRMO / PCG dashboard
Live SOS and acknowledgement Overdue review and drift contours Network and feed freshness
LGU / BFAR aggregated view
Consented coarse catch activity No identifiable safety trip trails Pilot workflow not field validated
ACK, ETA AND WARNINGS WHEN A RETURN PATH EXISTS
Responder acknowledgement creates ACKNOWLEDGED. Resolution remains a separate incident state.
Legend
Field / edge
Backend / data
Model / simulation
Emergency
External / human
Output
Fisheries
Solid: implemented software path Dashed: hardware, optional or return path awaiting field verification
Current status: software is locally tested; public deployment, real-device LoRa range and local field-model validation remain pending.
Notes: AqOne architecture sources:
README.md, current status and implemented versus unverified paths.
docs/55_HYBRID_TRANSPORT_ARCHITECTURE_DECISION.md, active boat-pod and direct-to-shore topology.
docs/06_DELIVERY_STATES.md, saved, relayed, delivered and acknowledged authorities.
docs/Aqone_PRD (2).md, canonical product and AI scope.
docs/17_AI_EXPLAINED_SIMPLY.md, squall, trip anomaly, drift and browser danger-zone implementation.
web/js/dashboard/dashboard-live-sos.js, current three-second REST polling behavior.