## Slide 1
AqOne System Data Paths
Separate tracks for SOS uplink, optional relay, direct internet and responder return
1 OF 3
Primary SOS uplink
Fisher phone
SQLite outbox State: SAVED
Boat pod
Flash queue State: RELAYED
Shore gateway
Signature verification Internet bridge
FastAPI and PostgreSQL
Validate, deduplicate, persist State: DELIVERED
MDRRMO dashboard
Displays SOS Responder authority
LOCAL WIFI HTTP
DIRECT LoRa
AUTHENTICATED HTTPS
REST POLLING
Optional relay route
Boat pod
Direct link unavailable
Relay buoy
TTL and seen-set forwarding
Shore gateway
Receives relayed frame
LoRa
LoRa
Direct internet route
Fisher phone
Internet available
FastAPI
Direct SOS ingest
HTTPS WHEN INTERNET IS AVAILABLE
Responder return path
Dashboard
Acknowledge and ETA
Backend
Persist response
Gateway
Queue downlink
Boat pod
Cache for phone
Fisher phone
State: ACKNOWLEDGED
WRITE
BACKHAUL
LoRa DOWNLINK
LOCAL STATUS
All shapes and connectors are editable PowerPoint objects
Solid line: software path Dashed line: optional or hardware path awaiting field verification
Notes: Sources: README.md; docs/55_HYBRID_TRANSPORT_ARCHITECTURE_DECISION.md; docs/06_DELIVERY_STATES.md; docs/04_INGEST_API.md; docs/05_PUBLIC_API.md.

## Slide 2
SOS Delivery and Acknowledgement
Numbered sequence with separate uplink and return tracks
2 OF 3
Uplink to responders
Phone saves SOS
Write to SQLite before network attempt
1
Pod queues SOS
Accept before phone acknowledgement
2
Gateway verifies
Verify signature and device identity
3
Backend commits
Deduplicate and persist the incident
4
Dashboard displays
Protected polling refreshes the feed
5
LOCAL WIFI HTTP
SIGNED LoAM FRAME
AUTHENTICATED HTTPS
REST POLLING
SAVED
RELAYED
DELIVERED
Responder action and return
Responder acknowledges
ETA, note and responder status
6
Backend stores response
Acknowledgement becomes authoritative
7
Gateway sends downlink
Queue response when a radio path exists
8
Pod exposes status
Phone reads cached acknowledgement
9
Phone reconciles
Show ACKNOWLEDGED only after evidence
10
PERSIST
BACKHAUL
LoRa DOWNLINK
LOCAL STATUS
ACKNOWLEDGED
If no return path exists, the handset keeps its last proven state. It never invents delivery or acknowledgement.
All shapes and connectors are editable PowerPoint objects
Solid line: software path Dashed line: optional or hardware path awaiting field verification
Notes: Sources: docs/06_DELIVERY_STATES.md; docs/03_PHONE_BUOY_WIFI.md; docs/04_INGEST_API.md; backend/app/api/sos.py; firmware/buoy/AqOneBuoy/AqOneBuoy.ino.

## Slide 3
AqOne Processing Pipelines
Each pipeline has its own lane, arrow color and output surface
3 OF 3
INPUT
QUALITY AND PREPARATION
MODEL OR CORE LOGIC
DECISION WORKFLOW
OUTPUT
MANUAL SOS
Phone or pod SOS
Human-triggered distress
Validate and deduplicate
Emergency intake remains unconditional
Persist incident
AI does not gate delivery
Responder acknowledgement
ETA, note and resolution
Dashboard and phone
Delivery state evidence
ENVIRONMENTAL WARNING
Pressure and weather
Fixed buoys plus Open-Meteo
Quality and freshness
Reject stale or insufficient input
Squall and danger models
Backend and browser inference
Advisory review
Official and human warnings take precedence
Mobile and dashboard
Warning with source and age
TRIP ANOMALY
Contacts and trip history
Routine vessel observations
Causal history filter
No future or candidate leakage
Per-vessel profile
Duration and route comparison
Verification and escalation
Silence alone does not prove distress
Responder review queue
Evidence and confidence
DRIFT AND SEARCH
Confirmed incident
Last reliable fix and object class
Environmental forcing
Wind, current and coastline
Monte Carlo leeway
Particle paths and uncertainty
Search posterior update
Negative search evidence
Search contours
50, 75 and 95 percent zones
CONSENTED CATCH ACTIVITY
Consented catch log
Separate optional purpose
Auth and validation
Safety access remains independent
Privacy aggregation
Coarse cells and reporter threshold
Recent activity surface
No guaranteed catch claim
Mobile and LGU view
No exact public positions
Manual SOS stays operational when every model is unavailable. Model outputs support authorized human decisions.
All shapes and connectors are editable PowerPoint objects
Solid line: software path Dashed line: optional or hardware path awaiting field verification
Notes: Sources: docs/Aqone_PRD (2).md; docs/17_AI_EXPLAINED_SIMPLY.md; docs/45_AI_PROSPECTIVE_EVALUATION_AND_CLAIMS.md; docs/07_SCOPE_OUT.md.